## Slide 1
Bio-Crypt Lock
A Risk-Adaptive Authentication System
Student: Roshini G | Roll No: 25BCE1676
Student: Sindhuja Bhaskar | Roll No: 25BCE5430
Student: K Aradhanaa | Roll No: 25BCE1994
Guide: Prof. Rathna R

## Slide 2
Agenda
01
Introduction
Why risk-adaptive authentication matters, the core idea, and how the system fits together.
02
Literature Survey
What existing research says about fingerprint, Bluetooth proximity, OTP, and adaptive authentication.
03
Challenges & Research Gap
The technical hurdles involved, and where current fixed-factor systems fall short.
04
Project Objectives
Six goals: biometric control, contextual risk awareness, dynamic OTP, adaptive logic, cryptographic verification, and logging.
05
Proposed Methodology & System Architecture
How the system works end to end, from a fingerprint scan to an adaptive access decision.
06
Results / Initial Implementation
Where development stands today: ESP32 setup, fingerprint integration, Bluetooth proximity, and workflow design.
2

## Slide 3
Introduction
Motivation & Core Concept
Most locks in use today still rely on a single factor — a fingerprint, a card, a PIN — which makes them easy to spoof, steal, or replay. Bio-Crypt Lock takes a different approach: it combines fingerprint biometrics, Bluetooth proximity as contextual information, and a dynamic OTP into one risk-adaptive workflow. Access is granted or denied based on how risky the situation looks, rather than a single fixed check.
Authentication Flow — the Risk-Adaptive Principle
Fingerprint → Risk Evaluation → Adaptive Authentication → Cryptographic Verification → Unlock / Deny
The fingerprint scan establishes identity. Bluetooth proximity adds context about the situation. A dynamic OTP is only brought in when the risk level rises — so security scales with the threat instead of slowing everyone down all the time.
Low risk: fingerprint + trusted Bluetooth → unlocks directly after cryptographic verification.
Medium risk: unfamiliar proximity → an OTP challenge is added before verification.
High risk: anomalous signals or failed attempts → stronger verification is required, or the system locks out temporarily.
3

## Slide 4
Literature Survey
Fingerprint Authentication
Jain et al. (2004) proposed minutiae-based fingerprint matching that performed well under constrained conditions, forming the basis of a lot of biometric identity verification since.
https://ieeexplore.ieee.org/document/1262027?utm_source=gemini
Maltoni et al. (2009) surveyed fingerprint liveness detection and spoofing countermeasures, pointing out how much harder robustness gets in real-world deployments.
https://link.springer.com/book/10.1007/978-1-84882-254-2?utm_source=gemini
Bluetooth & Proximity Auth
Madhavendra et al. (2019) used BLE RSSI for indoor proximity estimation, showing Bluetooth can serve as a reliable contextual signal for access control.
https://www.google.com/search?q=https://scholar.google.com/scholar%253Fq%253DMadhavendra%252BBLE%252BRSSI%252Bindoor%252Bproximity%252Bestimation%252B2019&utm_source=gemini
Bhatt & Bhatt (2021) integrated Bluetooth proximity with physical access systems and found that context-aware authentication cuts down on unauthorized entry.
https://www.google.com/search?q=https://scholar.google.com/scholar%253Fq%253DMadhavendra%252BBLE%252BRSSI%252Bindoor%252Bproximity%252Bestimation%252B2019&utm_source=gemini
OTP & Adaptive Auth
Bonneau et al. (2012) evaluated OTP schemes against phishing and replay attacks and confirmed time-based OTP as a strong second factor. https://www.google.com/search?q=https://ieeexplore.ieee.org/document/6234438&utm_source=gemini
Wiefling et al. (2021) proposed risk-based adaptive authentication that only asks for extra factors when needed, balancing security with convenience. https://www.google.com/search?q=https://ieeexplore.ieee.org/document/9442838&utm_source=gemini
Where this leaves us: the existing work treats biometrics, proximity, and OTP as separate problems. No single framework adapts its authentication requirements to real-time risk by combining all three — which is exactly the gap this project sets out to close.
4

## Slide 5
Challenges & Research Gap
Most authentication systems still lean on a single, fixed factor that doesn't account for how risky a situation actually is. Bio-Crypt Lock tries to close that gap by pulling biometric, proximity, and OTP signals into one adaptive workflow.
Key Challenges
Getting reliable fingerprint reads despite dirt, moisture, or angle
Treating Bluetooth proximity as context, not as a stand-alone identity check
Generating and delivering the dynamic OTP securely
Preventing replay attacks and enforcing OTP expiry
Handling failed attempts and lockout policy sensibly
Balancing strong security with everyday convenience
Research Gap
Biometric identity on its own doesn't account for context. Bluetooth proximity is useful as a risk signal, not as the sole authenticator. OTP should be invoked only when it's actually needed, not every single time. Fixed-factor systems apply the same checks no matter the risk level. Put simply: no existing low-cost embedded system brings fingerprint, Bluetooth, and conditional OTP together into one adaptive, cryptographically verified access-control workflow — and that's the gap this project fills.
5

## Slide 6
Project Objectives
1
Fingerprint-Based Identity Verification
Use fingerprint scanning as the primary identity layer — reliable, contactless user identification through an integrated fingerprint sensor and an ESP32 microcontroller, before any access decision gets made.
2
Dynamic OTP Generation
Generate a time-bound, one-time password on the fly whenever the risk-evaluation module flags suspicious or medium-risk conditions, so a static credential alone is never enough and every session needs fresh cryptographic proof.
3
Adaptive Authentication Requirements
Adjust how many factors are required — and which ones — based on the computed risk score: fingerprint only for low risk, OTP added for medium risk, and stronger verification or a temporary lockout for high risk.
4
Access-Event Logging
Log every access attempt, successful or denied, with a timestamp, the authentication factors used, and the assigned risk level — building an auditable trail for forensic review and for refining the adaptive thresholds over time.
6

## Slide 7
Proposed Methodology & System Architecture
Risk-Adaptive Workflow
Fingerprint Scan → Verification → Risk Evaluation → Adaptive Decision → Cryptographic Verification → Access Granted / Denied
Low Risk
Direct access
Medium Risk
Dynamic OTP invoked
High Risk
Stronger verification, or temporary lockout
System Architecture & Hardware
Hardware chain: Fingerprint Sensor → ESP32 → Risk Evaluation → Adaptive Authentication → Cryptographic Verification → Software Lock
Contextual inputs: Bluetooth Proximity feeds Risk Evaluation; the OTP Module supplies additional verification when triggered
Software: OTP validation engine, plus an access log / database for recording every event
7

## Slide 8
Results / Initial Implementation
Module 1 — Input Parameter Simulator
UI/CLI sliders or prompts for Fingerprint Optical Match Score (0–100%), BLE RSSI Signal Strength (−90 to −30 dBm), and Attempt History / Timestamp
Shows how the software inputs will stand in for hardware signals once those are wired up
Module 2 — Context Fusion & Dynamic Risk Engine
Fuses the input parameters into a Dynamic Risk Score (0–100) in real time
Routes access through a 3-tier protocol: Low (0–30) → direct unlock; Medium (31–70) → 6-digit TOTP challenge; High (71–100) → 8-digit challenge + lockout
Module 3 — Cryptographic File/Folder Decryption Engine
Demonstrates real file/folder encryption and decryption using AES-256, once risk verification succeeds
Access is only granted after both the authentication decision and the cryptographic verification pass
Module 4 — Anti-Replay Audit Logger
Records structured, timestamped authentication events: session ID, input signals, calculated risk score, and unlock status
Stores audit records in SQLite or CSV for traceability and later analysis
Demonstration: dynamic OTP generation • live risk-score computation • file/folder lock–unlock execution • audit-log generation
8